## Slide 1: Process Control Charts
Copyright (c) 2016 by The McGraw-Hill Companies. This spreadsheet is intended solely for educational purposes by licensed users of LearningStats. It may not be copied or resold for profit.

## Slide 2
Copyright Notice Portions of MINITAB Statistical Software input and output contained in this document are printed with permission of Minitab, Inc. MINITABTM is a trademark of Minitab Inc. in the United States and other countries and is used herein with the owner's permission.

## Slide 3: Common Control Charts
Note Variable charts are shown in blue, attribute charts in yellow, and zone charts in purple.

## Slide 4: Control Limits Illustrated
Centerline The intended target specification or historical mean
Lower Control Limit Sample means rarely are below LCL
Upper Control Limit Sample means rarely are above UCL
Copyright Notice Portions of MINITAB Statistical Software input and output contained in this document are printed with permission of Minitab, Inc. MINITABTM is a trademark of Minitab Inc. in the United States and other countries and is used herein with the owner's permission.

## Slide 5: Control Limits for X-Bar Chart

## Slide 6: Control Limits for R-Chart

## Slide 7: Example: Numerical Data
Example Manufactured tubing is to have a mean diameter of 15.00 mm. The historical standard deviation of the manufacturing process is 0.002 mm. Samples from 4 extrusion machines taken every 10 minutes and measured with precise instruments. The mean and range of the four sample items are plotted on control charts.
Comment X-Bar and R-charts are usually paired. The former reveals whether the process is tracking its centerline, while the latter reveals whether excessive variation exists.

## Slide 8: X-Bar/R Chart
Comment An X-bar chart reveals whether the process is tracking its centerline, while an R-chart reveals whether excessive variation exists. In this example, the process is in control, although the mean of sample 33 is very near its LCL.

## Slide 9: Example: Attribute Data
Example In a large urban hospital, a daily sample of 250 emergency arrivals is taken, showing the number of patients who were treated within 30 minutes. The historical proportion is 0.90.
Comment This requires either an np-chart (if we just count the number treated within 30 minutes) or a p-chart (if the count is converted to a proportion). The daily sample size must be constant in order to set the control limits.

## Slide 10: Example: np-Chart
Comment The centerline here is 225 (that is, 90% of 250). This chart indicates that, despite some fluctuation, the proportion treated within 30 minutes remains within its control limits.

## Slide 11: Example: p-Chart
Comment In this chart, the centerline is 0.90 (the target proportion is 90%). Except for scaling (dividing the total by 250) this p-chart is identical to the np-chart. Here, this sample proportion fluctuates, but remains within its control limits.

## Slide 12: Control Limits for np-Chart

## Slide 13: Control Limits for p-Chart

## Slide 14: I/MR Chart
Some manufacturing processes can be monitored continuously, obviating sampling. Each individual measurement is plotted on an I-chart. Since the sample size is n = 1, there is no range (R=Xmax-Xmin). Instead, we use a moving range and MR-chart. The control limits are explained in advanced texts.
Comment I-charts and MR-charts are usually paired. The former reveals whether the process is tracking its centerline, while the latter reveals whether excessive variation exists.

## Slide 15: I/MR Chart: Example
Example Manufactured tubing is to have a mean diameter of 15.00 mm. The historical standard deviation of the manufacturing process is 0.002 mm. A laser monitoring system eliminates the need for sampling, and measurements are taken automatically every minute. The observed diameter measurement and moving range are plotted on control charts.

## Slide 16: Example: Tubing Diameter
Comment The process is tracking its centerline (I-chart) and variation does not appear excessive (MR-chart).

## Slide 17: X-Bar Chart Tests for Pattern
Rule 1 Single point beyond 3 sigma
Rule 2 2 of 3 successive points beyond 2 sigma on same side of centerline
Rule 3 4 of 5 successive points beyond 1 sigma on same side of centerline
Rule 4 9 successive points on same side of centerline

## Slide 18: Rule 1
Rule 1 Single point beyond 3 sigma
out of control

## Slide 19: Rule 2
Rule 2 2 of 3 successive points beyond 2 sigma on same side of centerline
out of control

## Slide 20: Rule 3
Rule 3 4 of 5 successive points beyond 1 sigma on same side of centerline
out of control

## Slide 21: Rule 4
Rule 4 9 successive points on same side of centerline
out of control

## Slide 22: Other Pattern Tests
Note Other rules of thumb are possible. Here are MINITAB’s versatile tests for pattern for X-bar/R charts.

## Slide 23: Violations
Cycle Observations follow a cyclic pattern (several above centerline followed by several below the centerline). Detected visually or by runs test.
Oscillation Observations tend to alternate above and below the centerline. Detected visually or using a runs test.
Instability Observations vary more than expected so the points lie too far from the centerline. Detected by rules 1-3 or from the R-chart.
Level shift Observations shift abruptly to a level above (or below) the centerline and then stay there. Detected by rules 1-4. Can resemble trend.
Trend Observations drift slowly either upward or downward. Detected by rules 1-4 or by visual inspection. Can resemble level shift.
Mixture Observations come from two or more populations which are different. Similar to instability. May be hard to detect.

## Slide 24: Instability
Test Results for I Chart
TEST 5. 2 out of 3 points more than 2 sigmas from center line
Test Failed at points: 66 98
TEST 6. 4 out of 5 points more than 1 sigma from center line
Test Failed at points: 87 98 99
Test Results for MR Chart
TEST 1. One point more than 3.00 sigmas from center line.
Test Failed at points: 65 67 77 78

## Slide 25: Trend
Test Results for I Chart
TEST 2. 9 points in a row on same side of center line.
Test Failed at points: 12 86 87 88 89 90 91 92 93 94
Test Results for MR Chart
TEST 2. 9 points in a row on same side of center line.
Test Failed at points: 10 11 12 13 14
Note Easily mistaken for level shift.

## Slide 26: Level Shift
Test Results for I Chart
TEST 2. 9 points in a row on same side of center line.
Test Failed at points: 49 87 97 98 99
Test Results for MR Chart
TEST 2. 9 points in a row on same side of center line.
Test Failed at points: 30
Note Easily mistaken for trend.

## Slide 27: Cycle
Comment Visual inspection suggests series of runs above centerline followed by series of runs below centerline. For a chart showing m samples, the expected number of centerline crossings would be roughly m/2 +1. For these 50 samples, we see only 19 crossings but would expect 26.

## Slide 28: Oscillation
Visual inspection suggests alternating means above and below centerline. For a chart showing m samples, the expected number of centerline crossings would be roughly m/2 +1. For these 50 samples, we see 40 crossings but would expect only 26 (it’s hard to count some of the crossings but we’ll call it 40).

## Slide 29: Runs Test
Patterns of cycle and oscillation may not violate any of the usual rules. A more sensitive test for cycle or oscillation is the runs test. For m samples, the expected number of centerline crossings is m/2+1. If m is reasonably large, we count the actual number of centerline crossings R and compute a test statistic:
If m is reasonably large, an approximate result is:

## Slide 30: Runs Test: Example
For 50 samples, we observe 40 centerline crossings. The runs test statistic is:
Since m is reasonably large, the approximate normal test statistic is:
Either result shows that the observed number of runs is almost four standard deviations above its expectation, suggesting that oscillation exists (positive sign). A negative sign would suggest cycle.

## Slide 31: Other Control Charts
Note There are many types of control charts. Here are some offered by MINITAB. If you want to learn about them, you’ll need to take a specialized class.
Variable charts for subgroups
Variable charts for individuals
Time-weighted variable charts
Attribute charts

## Slide 32: Service Sector?
In services such as health care, the usual control charts may not apply because
  processes may not be repetitive
  sample size may vary from sample to sample
  sample intervals may be irregular
  t here is no a priori benchmark to meet.
Alternatives include (1) a time plot showing a statistic surrounded by its confidence interval (e.g., mean or proportion), (2) a box plot over time (for a numerical variable such as waiting time), or (3) a plot of percentiles of the raw data over time (e.g., 10, 25, 50, 75, 90).

## Slide 33: Simple Time Plot

## Slide 34: Hi-Lo Plot

## Slide 35: Box Plots Over Time

## Slide 36: Summary
Control charts help you track change
Control charts were developed for manufacturing
Control charts can also be used in services
Creative modifications may be needed